## Slide 1
© 2013 California Institute of Technology. Government sponsorship acknowledged.
2013 IEEE Aerospace Conference
Andrea Donnellan (JPL)
Integrating Remotely Sensed and Ground Observations for Modeling, Analysis, and Decision Support
Margaret Glasscoe, Jay Parker, Robert Granat (JPL)
Marlon Pierce, Jun Wang, Geoffrey Fox (Indiana University)
Dennis McLeod (University of Southern California)
John Rundle, Eric Heien (UC Davis)
Lisa Grant Ludwig (UC Irvine)

## Slide 2
Earthquake science and emergency response require integration of many data types and models that cover a broad range of scales in time and space
Timely and efficient earthquake analysis and response require automated processes and a system in which the interfaces between models and applications are established and well defined
Geodetic imaging data provide observations of crustal deformation from which strain accumulation and release associated with earthquakes can be inferred
Data products are growing and tend to be either relatively large in size, on the order of 1 GB per image with hundreds or thousands of images, or high data rate, such as from 1 second GPS solutions
Products can be computationally intensive to manipulate, analyze, or model, and are unwieldy to transfer across wide area networks
Required computing resources can be large, even for a few users, and can spike when new data are made available or when an earthquake occurs
A cloud computing environment is the natural extension for some components of QuakeSim as an increasing number of data products and model applications become available to users
Storing the data near the model applications improves performance for the user

## Slide 3
Forecasting
Mitigating losses through preparedness and targeted retrofitting
Current Forecast
Response
Virginia Earthquake
Damage assessment
Impact to critical infrastructure
Understanding
Creeping faults
Location and size of future earthquakes, stress transfer and fault interactions
Computational infrastructure for integrating remotely sensed and other data with mapping, modeling, and analysis tools for understanding earthquake processes

## Slide 4: Workflow
Data Products Providers
Applications
Outputs
Fault geometries
Fault slip rates
Strain migration
Earthquake fault behavior
Crustal deformation anomalies
Earthquake likelihood
Crustal Deformation
Earthquake fault system simulators
Forecast
Time series analysis
Faults
Scientific publications, official data sets,
inferred from models
Seismicity
USGS, SCSN, NCSN, ANSS
GPS
JPL, SOPAC, UNAVCO, UNR
InSAR/UAVSAR
JPL, ASF
Raw data
Response
Notes: QuakeSim inputs, outputs, and feedback to data providers. Multiple data products are used from numerous providers. These are used in applications for understanding faults and forecasting earthquake likelihood. At times output from the applications identifies issues with the data products, which can be in the form of previously unrecognized faults, unmodeled error sources, or processing issues.

## Slide 5: A Brief History
132
Direction
China Seismometer
1855
Time, Duration
Intensity
Luigi Palmieri, Italy
1880
Waveforms
Milne, Ewing, Gray:
British professors
in Japan
Wegner
1915
Continental Drift
1935
Intensity of earthquake
Richter Scale
Hanks & Kanamori
1979
Moment Magnitude
Area x Slip x Rigidity
L
W
Slip
0
2000
1000
1500
500
AD
Space Geodesy
1984
Measured plate tectonics

## Slide 6: Earthquakes Occur over Many Scales
Plate Tectonics – Global/millennia
Strain accumulation – kilometers/decades
Earthquakes – nucleate over meters/milliseconds
Postseismic adjustment – kilometer/month scales
Magnitude 7 in California: $200-300B losses and thousands of lives

## Slide 7: Geodesy Observes the Earthquake Cycle
Strain accumulation and release

## Slide 8: Geodetic Imaging Products
GPS
  Smooth in time, not space
InSAR
  Smooth in space, not time
Epoch 0
Epoch n
GPS Position Series
InSAR

## Slide 9: GPS
Horizontal position accuracy 1 mm
Vertical position accuracy 2 mm
1 mm/yr horizontal velocities

## Slide 10: GPS Position Time Series Analysis
Substantial postseismic motion northeast of the El Mayor – Cucapah Rupture

## Slide 11: California GPS Deformation
Los Angeles

## Slide 12: Visualizing Crustal Deformation

## Slide 13: Salton Trough
Two years before the 2010 M 7.2 El Mayor – Cucapah Earthquake
Reference

## Slide 14: Salton Trough
Two days before the 2010 M 7.2 El Mayor – Cucapah Earthquake
Regional shear

## Slide 15: Salton Trough
Three days after the 2010 M 7.2 El Mayor – Cucapah Earthquake
Coseismic

## Slide 16: Salton Trough
Two months after the 2010 M 7.2 El Mayor – Cucapah Earthquake
Postseismic shear

## Slide 17: Salton Trough
Seven months after the 2010 M 7.2 El Mayor – Cucapah Earthquake
Postseismic shear

## Slide 18: Salton Trough
Two years before the 2010 M 7.2 El Mayor – Cucapah Earthquake
Reference
2 years

## Slide 19: Salton Trough
Two days before the 2010 M 7.2 El Mayor – Cucapah Earthquake
Regional shear
5 days
2 years

## Slide 20: Salton Trough
Three days after the 2010 M 7.2 El Mayor – Cucapah Earthquake
Coseismic
2 months
5 days

## Slide 21: Salton Trough
Two months after the 2010 M 7.2 El Mayor – Cucapah Earthquake
Postseismic shear
1.3 years
2 months

## Slide 22: Salton Trough
1 ½ years after the 2010 M 7.2 El Mayor – Cucapah Earthquake
Postseismic shear
1.3 years

## Slide 23: Visualizing Crustal Deformation

## Slide 24: Earthquake Response
Modeled San Andreas fault earthquake scenario (ShakeOut 2008)
Tilt maps show where water and sewer lines may run backwards for an event on the Cucamonga Fault (Golden Guardian 2012)

## Slide 25: Decision Support

## Slide 26: UAVSAR
L-band radar
Flies on a Gulfstream III aircraft

## Slide 27: Image of 2010 M 7.2 Earthquake in Baja
California-Mexico Border
California-Mexico Border
Each fringe represents 12 cm displacement to/from instrument
Lower plot shows total displacement to/from the instrument

## Slide 28: Creep Occurred on Faults to the North
Superstition Hills Fault
Imperial Fault
P503
Chart: 
P503 | -4.5761
1 cm
Chart: 
2.3 cm

## Slide 29: Complex Pattern of Fault Slip
What are the implications for stress accumulation on the San Andreas Fault?

## Slide 30: Clouds
Centralization of computing capacity into highly scalable data centers
Cloud Computing provides potentially greater computing capacity but with larger latencies compared to traditional high performance computing
Good for “big data” problems in which the same operations need to be performed on very large data sets
  Little communication between individual processes or movement of data is needed
The earthquake problem is highly scalable
  Earthquake events or new data can result in spikey usage
  Model and simulation runs can be quite large
Applications
  InSAR geodetic imaging data as volumes grow over time
  High rate GPS data products
  Simulations and inversions where similar runs are done with different initial conditions

## Slide 31: Infrastructure as a Service
Virtual Machines to provide access to hosted servers and resources that appear to the user as “just another server”
Resources are elastic and can be scaled up or down as needed
  Event driven for QuakeSim
    Earthquake
    New data products

## Slide 32: Platform as a Service
Allows the user to deploy user-created applications within a specific cloud framework into the cloud for use by others

## Slide 33: Software as a Service
The cloud provider provides a specific capability or software to the user
Individual services corresponding to different QuakeSim tools
  InSAR profiles
  Forward and inverse models
  GPS time series analysis
GPS time series state changes after the 2010 M 7.2 El Mayor-Cucapah earthquake

## Slide 34: Virtual California
Simulating earthquake fault interactions

## Slide 35: Web Coverage Service (WCS) Performance
OGC standard to retrieve raster data based on spatial constraints and other query criteria
Testing procedure
  Randomly choose one InSAR image
  Randomly generate a small rectangle bounding box inside an InSAR image
  Send a request to GeoServer and retrieve the image in GeoTiff
Performance is measured by the average response time of one user request call, which includes GeoServer response time and network transfer time
 | Test Client from IU |  | Test Client from Amazon | 
 | IUII | Amazon | IUII | Amazon
Native Resolution | 0.57 | 1.28 | 1.30 | 0.54
Resample | 0.27 | 0.73 | 0.70 | 0.23
Resample + ReProjection | 0.34 | 0.78 | 0.71 | 0.24

## Slide 36: Virtual California Performance
Parallel scaling and performance analysis on FutureGrid test bed
3000 year simulation runs are shown on “bare metal” (regular MPI) and OpenStack (Cloud)
At the bottom results are presented on 2, 4, 8, 16, 32, 64 and 128 cores for compute-communication fractions
  Regular MPI on the left
  OpenStack on the right

## Slide 37: Summary
QuakeSim has several components
  Model applications
  Analysis tools
  Map browsers
  Data product access
Several Interfaces
  Organizations and their data products
  Internal interfaces to database, map viewer, applications
Clouds are a promising new method for analysis and modeling of large data product sets and for multiple parallel runs
  In some instances it may be better to use standard resources instead of clouds
  Careful consideration should be given to what resources to use for various tasks
Collaboration between QuakeSim developers, data product providers, and downstream consumers early on will result in improved efficiency
http://quakesim.org