## Slide 1: Hadoop-Harp Applications Performance Analysis on Big Red II

## Slide 2: Notes
For K-Means Clustering and FR Graph Drawing Algorithm,
I use execution time and speedup to explain the performance because
  They can be drawn in one picture.
  Due to the intensive computation, I find these applications are easy to achieve linear speedup when the number of nodes is small. Therefore the parallel efficiency is always around 1.

## Slide 3: K-Means Clustering Execution Time and Speedup on Big Red II (10 Iterations Benchmark, Nodes: 8, 16, 32, 64, 128, JVM settings: -Xmx44000m –Xms44000m -XX:NewRatio=1 -XX:SurvivorRatio=98)
Chart: Number of Nodes
| 8 | 16 | 32 | 64 | 128
500m points 10k centroids Execution Time | 3680.7545 | 1749.3945 | 903.093 | 444.507 | 252.1065
5m points 1m centroids Execution Time | 5334.8255 | 2845.961 | 1216.665 | 624.126 | 342.5375
500m points 10k centroids Speedup | 8 | 16.8321 | 32.6058 | 66.2443 | 116.8
5m points 1m centroids Speedup | 8 | 14.9962 | 35.0784 | 68.3814 | 124.5954

## Slide 4: FR Graph Drawing Algorithm Execution Time and Speedup on Big Red II (477111 Vertices and 665599 Undirected Edges, 10 Iterations Benchmark, Nodes: 1, 8, 16, 32, 64, 128, JVM settings: -Xmx44000m –Xms44000m -XX:NewRatio=1 -XX:SurvivorRatio=98)
Chart: Number of Nodes
| 1 | 8 | 16 | 32 | 64 | 128
Execution Time | 8988.919 | 1078.6027 | 583.4557 | 315.5767 | 162.021 | 90.424
Speedup | 1 | 8.3339 | 15.4063 | 28.4841 | 55.48 | 99.4086

## Slide 5: WDA-SMACOF Execution Time on Big Red II (Full Application Benchmark, Nodes: 8, 16, 32, 64, 128, JVM settings: -Xmx54000m -Xms54000m, -XX:NewRatio=1 -XX:SurvivorRatio=98)
Chart: Number of Nodes
| 8 | 16 | 32 | 64 | 128
100k points | 1952.3558 | 1041.6363 | 531.2175 | 315.0508 | 230.5572
200k points | 2654.25 | 1519.6539 | 765.8065
300k points | 3572.093 | 2081.0853
400k points | 3252.0244

## Slide 6: WDA-SMACOF Parallel Efficiency on Big Red II (Full Application Benchmark, Nodes: 8, 16, 32, 64, 128, JVM settings: -Xmx54000m -Xms54000m -XX:NewRatio=1 -XX:SurvivorRatio=98)
Chart: Number of Nodes
| 8 | 16 | 32 | 64 | 128
100k points | 1 | 0.93716 | 0.91881 | 0.77462 | 0.52925
200k points | 1 | 0.87331 | 0.86649
300k points | 1 | 0.85823

## Slide 7: WDA-SMACOF Speedup on Big Red II (Full Application Benchmark, Nodes: 8, 16, 32, 64, 128, JVM settings: -Xmx54000m -Xms54000m -XX:NewRatio=1 -XX:SurvivorRatio=98)
Chart: Speedup
| 8 | 16 | 32 | 64 | 128
100k points | 8 | 14.9945 | 29.402 | 49.5756 | 67.7439
200k points | 32 | 55.8917 | 110.9105
300k points | 64 | 109.8532