## Slide 1: Panda: MapReduce Framework on GPU’s and CPU’s
Hui Li
Geoffrey Fox

## Slide 2: Research Goal
provide a uniform MapReduce programming model that works on HPC Clusters or Virtual Clusters cores on traditional Intel architecture chip, cores on GPU.
CUDA, OpenCL, OpenMP, OpenACC
Notes: Traditional CPUs, whose cores are optimized for single-threaded performance, are not designed for work requiring lots of throughput FPGA
For that type of computing, much better energy efficiency can be delivered using simpler, slower, but more numerous cores. Both GPUs and the MIC adhere to this paradigm;

## Slide 3: Multi Core Architecture
Sophisticated mechanism in optimizing instruction and caching
Current trends:
  Adding many cores
  More SIMD: SSE3/AVX
  Application specific extensions: VT-x, AES-NI
  Point-to-Point interconnects, higher memory bandwidths
Notes: - Single core performance gains stagnating
- Focusing more on power optimizations, mobility

## Slide 4: Fermi GPU Architecture
Generic many core GPU
Not optimized for single-threaded performance, are designed for work requiring lots of throughput
Low latency hardware managed thread switching
Large number of ALU per “core” with small user managed cache per core
Memory bus optimized for bandwidth

## Slide 5: GPU Architecture Trends
Throughput Performance
Programmability
CPU
GPU
Figure based on Intel Larabee Presentation at SuperComputing 2009
Fixed Function
Fully Programmable
Partially Programmable
Multi-threaded
Multi-core
Many-core
Intel Larabee NVIDIA CUDA

## Slide 6: Top 10 innovations in NVIDIA Fermi GPU and top 3 next challenges
 | Top 10 innovations | Top 3 next challenges
1 | Real floating point in Quality and performance | The Relatively Small Size of GPU memory
2 | Error correcting codes on Main memory and Caches | Inability to do I/O directly to GPU memory
3 | Fast Context Switching | No Glueless multi-socket hardware and software
4 | Unified Address Space | (Programmability ?)
5 | Debugging Support | 
6 | Faster Atomic Instructions to Support Task-Based Parallel | 
7 | Caches | 
8 | 64-bit Virtual Address Space | 
9 | A Brand new Instruction Set | 
10 | Fermi is faster than G80 | 

## Slide 7: GPU Clusters
GPU clusters hardware systems
  FutureGrid 16-node Tesla 2075 “Delta” 2012
  Keeneland 360-node Fermi GPUs 2010
  NCSA 192-node Tesla S1070 “Lincoln” 2009
GPU clusters software systems
  Software stack similar to CPU cluster
  GPU resources management
GPU clusters runtimes
  MPI/OpenMP/CUDA
  Charm++/CUDA
  MapReduce/CUDA
  Hadoop/CUDA

## Slide 8: GPU Programming Models
Shared memory parallelism (single GPU node)
  OpenACC
  OpenMP/CUDA
  MapReduce/CUDA
Distributed memory parallelism (multiple GPU nodes)
  MPI/OpenMP/CUDA
  Charm++/CUDA
  MapReduce/CUDA
Distributed memory parallelism on GPU and CPU nodes
  MapCG/CUDA/C++
  Hadoop/CUDA
    Streaming
    Pipelines
    JNI (Java Native Interface)

## Slide 9: GPU Parallel Runtimes
Name | Multiple GPUs | Fault Tolerance | Communication | GPU Programming Interface
Mars | No | No | Shared | CUDA/C++
OpenACC | No | No | Shared | C,C++,Fortran
GPMR | Yes | No | MVAPICH2 | CUDA
DisMaRC | Yes | No | MPI | CUDA
MITHRA | Yes | Yes | Hadoop | CUDA
MapCG | Yes | No | MPI | C++

## Slide 10: CUDA: Software Stack
Image from [5]

## Slide 11: CUDA: Program Flow
Application Start
Search for CUDA Devices
Load data on host
Allocate device memory
Copy data to device
Launch device kernels to process data
Copy results from device to host memory
CPU
Main Memory
Device Memory
GPU Cores
PCI-Express
Device
Host

## Slide 12: CUDA: Thread Model
Kernel
  A device function invoked by the host computer
  Launches a grid with multiple blocks, and multiple threads per block
Blocks
  Independent tasks comprised of multiple threads
  no synchronization between blocks
SIMT: Single-Instruction Multiple-Thread
  Multiple threads executing time instruction on different data (SIMD), can diverge if neccesary
Image from [3]

## Slide 13: CUDA: Memory Model
Image from [3]
Notes: Avoid task switching overhead by statically allocating thread resources

## Slide 14: Panda: MapReduce Framework on GPU’s and CPU’s
Current Version 0.2
Applications:
  Word count
  C-means clustering
Features:
  Run on two GPUs cards
  Some initial iterative MapReduce support
Next Version 0.3
Features:
  Run on GPU’s and CPU’s (done for word count)
  Optimized static scheduling (todo)

## Slide 15: Panda: Data Flow
CPU Cores
CPU Memory
GPU Memory
GPU Cores
PCI-Express
GPU accelerator group
Panda Scheduler
CPU
Memory
CPU Cores
CPU processor group
Shared memory

## Slide 16: Architecture of Panda Version 0.3
GPU Accelerator Group 1
GPUMapper<<<block,thread>>>
Round-robin Partitioner
Copy intermediate results of mappers from GPU to CPU memory; sort all intermediate key-value pairs in CPU memory
Merge Output
Configure Panda job, GPU and CPU groups
Static scheduling based on GPU and CPU capability
Iterations
GPU Accelerator Group 2
GPUMapper<<<block,thread>>>
Round-robin Partitioner
CPU Processor Group 1
CPUMapper(num_cpus)
Hash Partitioner
3
16
5
6
12
10
13
7
2
11
15
4
9
16
8
1
1
2
3
4
6
5
7
8
9
10
12
11
13
14
15
16
GPU Accelerator Group 1
GPUReducer<<<block,thread>>>
Round-robin Partitioner
GPU Accelerator Group 2
GPUReducer<<<block,thread>>>
Round-robin Partitioner
CPU Processor Group 1
CPUReducer(num_cpus)
Hash Partitioner
Static scheduling for reduce tasks

## Slide 18: Panda’s Performance on GPU’s
2 GPU: T2075
C-means Clustering (100dim,10c,10iter, 100m)
Chart: 
Mars 1GPU | 29.4 | 58.3 | 86.9 | 116.2 | 145.78
Panda 1 GPU | 18.2 | 35.95 | 53.26 | 71.3 | 90.1
Panda 2 GPU | 9.76 | 18.56 | 27.2 | 36.31 | 45.5

## Slide 19: Panda’s Performance on GPU’s
1 GPU T2075
C-means clustering (100dim,10c,10iter,100m)
Chart: 
| 100k | 200k | 300k | 400k | 500k
without iterative support | 18.2 | 35.95 | 53.26 | 71.3 | 90.1
with iterative support | 6.7 | 8.8 | 12.95 | 15.89 | 18.7

## Slide 20: Panda’s Performance on CPU’s
20 CPU Xeon 2.8GHz; 2GPU T2075
Word Count Input File: 50MB
Chart: 
2GPU+20CPU | 35.77
2GPU | 40.7
1GPU+20CPU | 121.1
1GPU | 146.6

## Slide 21: Acknowledgement
FutureGrid
SalsaHPC