## Slide 1: Videoconferencing Systems
Tom Stachowiak
CPS 640
Syracuse University
Spring 1998

## Slide 2: Videoconferencing Systems Outline
  Multimedia technologies
    compression
    standards
  Existing products overview
  Issues in design and implementation
    system objectives
    architecture
    components description
http://trurl.npac.syr.edu/toms/Publications/Thesis/Thesis.html

## Slide 3: Technology Data Compression
Reduction of the amount of allocated space
Two basic classes of compression
  redundancy reduction - does not introduce distortions
  entropy reduction - information losses
Standard algorithms are not efficient for audiovisual signals

## Slide 4: Technology Audio Compression
Adaptive Differential Pulse Code Modulation (ADPCM)
    lower variance of difference between samples
    linear prediction
    locally stationary audio signals
    adaptive corrections to prediction coefficients
    minimizing the Mean Square Error (MSE)

## Slide 5: Technology Audio Compression
GSM speech compression
    cellular telephony standard
    designed specifically for the speech signals
    based on Long-Predictive Coding (LPC)
    modeling of the human vocal tract with an adaptive filter
    transmitted data:
      filter coefficients
      general characteristics of the signal(e.g. gain, lag)
      residual pulse excitation

## Slide 6: Technology Video Compression
ITU-T H.261 algorithm
    Discrete Cosine Transform (DCT) coding technique
    uses two video compression methods
      spatial redundancy removal (every frame)
      temporal redundancy removal (INTER frames)
    two types of frames
      INTRA - coded independently
      INTER - predicted coding based on the previous frame

## Slide 7: Technology H.261 Video Compression
Bitstream structure
Motion vector search
  full spiral search
  logarithmic search
INTRA frame coding

## Slide 8: Technology H.263 Video Compression
  Modified version of H.261
  Improvements:
    half-pixel motion vector prediction
    modified Variable Length Coding (VLC) tables
    negotiable options
      unrestricted motion vector
      advanced prediction
      arithmetic coding instead of VLC
      PB-frames

## Slide 9: Technology Multimedia standards
  Data transmission standards
    Real-Time Protocol (RTP)
      designed for the audiovisual data
      does not guarantee quality of service
      functionality:
        payload type identification
        sequence numbering
        timestamping
        delivery monitoring
      augmented by RTCP
        loosely coupled conference control
        data transmission reports

## Slide 10: Technology Session control standards
International Telecommunication Union (ITU)
  ITU Telecommunication Standardization Section (ITU-T)
    Series H Recommendations - line transmission of non-telephone signals
    Series T Recommendations - terminal characteristic and higher level protocols for telematic equipment

## Slide 11: Technology Session control standards
ITU-T H.323 - visual telephone systems and equipment for LAN without guaranteed quality of service

## Slide 12: Session control standards ITU-T H.323
  Control protocols
    H.245
      master/slave determination
      capabilities exchange
      logical channel signaling
    H.225
      call control
      gatekeeper related functions

## Slide 13: Session control standards ITU-T H.323
  Visual telephone system components definitions:
    terminals
      creating two-way, real-time channels
      communication control
      indications
      audio and video
      data transportation

## Slide 14: Session control standards ITU-T H.323
    Gateways
      conversion between data formats and control protocols
      a bridge between LANs and switched circuit networks (e.g. ISDN)
      transparent for endpoints
    Gatekeepers
      optional
      logically separate component
      physically can be combined with terminal, gateway or MCU

## Slide 15: Session control standards ITU-T H.323
    Gatekeepers
      functionality
        address translation (alias - transport)
        admission control
        bandwidth control
        zone management
        call management
    Multipoint Controllers (MC)
      creating and managing conferences between three or more endpoints
      capabilities exchange
      located in MCU, terminal, gateway or gatekeeper

## Slide 16: Session control standards ITU-T H.323
    Multipoint Processors (MP)
      converting audio, video and data streams
      format changes
      multiplexing/demultiplexing
      usually located in MCU together with MC
    Multipoint Control Units (MCU)
      multipoint conferences support
      consists of MC and several MPs
      centralized, decentralized or hybrid multipoint capabilities
      additional operations (e.g. rate matching, lip synchronization)

## Slide 17: Technology Session control standards
ITU-T T.120 - protocol integrating multiple data formats in multipoint conference
  series of recommendations defining multipoint data conference
    session establishment
    participants identifications and capabilities exchange
    communication channels management

## Slide 18: Technology ITU-T T.120

## Slide 19: Technology ITU-T T.120

## Slide 20: Technology ITU-T T.120
T.120 layered structure
  Multipoint Communication Service (MCS)
    collects point-to-point connections to form multipoint channels
    tree structure
    transparent resource provider
    channel types:
      static - preassigned definition, open
      dynamic - created on request
        multicast - open
        private - owner, joining by invitation only

## Slide 21: Technology ITU-T T.120
  Multipoint Communication Service (MCS)
    data types
      ordinary data - shortest route, different order possible
      uniform sequenced data - sent through a common point, received in the same order by all users
  User application
    generic application template
    set of protocols for the most popular applications

## Slide 22: Technology ITU-T T.120
  Generic Conference Control (GCC)
    set functions for managing conferences
    combining independent MCS channels into one multipoint domain
    central point for identifying channels, applications and capabilities
  Node controller
    user interface for conference management functions

## Slide 23: Videoconferencing Products Examples
Videotelephones
  point-to-point
  RTP
  partial H.323
  examples:
    Intel Internet Videophone
    IBM BambaPhone

## Slide 24: Videoconferencing Products Examples
Videoconferencing Systems
  CU-SeeMe
    H.323 support
    reflectors
    directory service
    one platform only (Windows 95/NT)
  Vic/Vat
    multiplaform (beta on Windows 95/NT)
    variety of compression algorithms
    modular (SD, Vic, Vat)

## Slide 25: Videoconferencing Products Summary
Disadvantages:
  single platform
  point-to-point only
  proprietary compression
  lack of flexibility

## Slide 26: Design and Implementation System Objectives
Flexibility
Interoperability
  platform interoperability
  implementation interoperability
Extensibility
Archiving capability

## Slide 27: Design and Implementation System Architecture
Physical System Components

## Slide 28: Design and Implementation System Architecture
Logical System Structure

## Slide 29: Design and Implementation System Architecture
Multipoint Communication Layer (MCL)
  reliable multipoint channels
  unreliable multipoint channels
Session Control Layer (SCL)
  implemented inside the Conference Engine
  events distribution and handling
  conference information management

## Slide 30: Design and Implementation System Architecture
RTP Layer
  effective processing of media streams
  providing useful information for real-time purposes
Session API
  functions for conference creation and management
  covers the internal manager-engine protocol

## Slide 31: Design and Implementation System Architecture
Application API
  provides useful mechanism for creating new conference application
  developer is concerned only about the data presentation
  important element of system extensibility

## Slide 32: Design and Implementation System Architecture
Session Control Protocol (SCP)
  conference participants management
  conference applications management
  maintaining additional information:
    users directory interconnection
    token mechanism

## Slide 33: Design and Implementation Conference Applications
Audio Tool
Video Tool
Whiteboard
Text Chat
mechanisms for porting arbitrary application

## Slide 34: Design and Implementation Audio Tool
Compression:
  GSM (13 kbps)
  ADPCM (32 kbps)
  PCM (128 kbps)
Architecture
Half-duplex support
Streams buffering and multiplexing

## Slide 35: Design and Implementation Video Tool
Compression:
  H.263 low bandwidth, CPU intensive
  H.261
  H.261 intra - only INTRA frames
  YUV9
Architecture similar to Audio Tool
Frame rate control
Formats conversion

## Slide 36: Design and Implementation Video Tool
Adapting H.261/H.263 codecs
  creating library
  single frame procedures
  converting I/O
  multiple streams handling
  inserting INTRA frame
  performance improvement:
    logarithmic search

## Slide 37: Design and Implementation Directory Service
Active nodes monitoring
On-going sessions advertising
conference creation facilitating
protection and security
session types:
  open
  password protected
  master controlled

## Slide 38: Design and Implementation Archiving
Asynchronous storage mode
System integration:
  application API
  session API
  engine
Database integration

## Slide 39: Design and Implementation Other issues
Java API
  extensibility feature
  multiplatform application
  proof of system flexibility
Session security
  close control model
  data confidentiality
  directory security

## Slide 40: Design and Implementation Web Integration
Tango as collaborative Java environment
BuenaVista vs. Tango
Modifications

## Slide 41: Conclusions System Advantages
Multiuser
Multiplatform
Extensibility
  modular structure
  multilanguage support (APIs)

## Slide 42: Conclusions System Advantages
Flexibility
  several operating modes
  bandwidth control
  Web integration
Archiving capabilities
Interoperability
  standard compliance

## Slide 43: Conclusions Disadvantages and Future Work
Lack of full standard compliance (H.323)
Robustness
Only one session per host
Graphical User Interface (GUI)