## Slide 1: Videoconferencing System
Master’s Thesis
Tomasz Stachowiak

## Slide 2: Videoconferencing System Presentation Outline
  Multimedia technologies
    compression
    standards
  Existing products overview
  Design and implementation
    system objectives
    architecture
    components description
  Conclusions

## Slide 3: Technology Data Compression
Reduction of the amount of allocated space
Two basic classes of compression
  redundancy reduction - does not introduce distortions
  entropy reduction - information losses
Standard algorithms are not efficient for audiovisual signals

## Slide 4: Technology Audio Compression
Adaptive Differential Pulse Code Modulation (ADPCM)
    lower variance of difference between samples
    linear prediction
    locally stationary audio signals
    adaptive corrections to prediction coefficients
    minimizing the Mean Square Error (MSE)

## Slide 5: Technology Audio Compression
GSM speech compression
    cellular telephony standard
    designed specifically for the speech signals
    based on Long-Predictive Coding (LPC)
    modeling of the human vocal tract with an adaptive filter
    transmitted data:
      filter coefficients
      general characteristics of the signal(e.g. gain, lag)
      residual pulse excitation

## Slide 6: Technology GSM Audio Compression

## Slide 7: Technology Video Compression
ITU-T H.261 algorithm
    Discrete Cosine Transform (DCT) coding technique
    uses two video compression methods
      spatial redundancy removal (every frame)
      temporal redundancy removal (INTER frames)
    two types of frames
      INTRA - coded independently
      INTER - predicted coding based on the previous frame

## Slide 8: Technology H.261 Video Compression
Bitstream structure
Motion vector search
  full spiral search
  logarithmic search
INTRA frame coding

## Slide 9: Technology H.263 Video Compression
  Modified version of H.261
  Improvements:
    half-pixel motion vector prediction
    modified Variable Length Coding (VLC) tables
    negotiable options
      unrestricted motion vector
      advanced prediction
      arithmetic coding instead of VLC
      PB-frames

## Slide 10: Technology Multimedia standards
  Data transmission standards
    Real-Time Protocol (RTP)
      designed for the audiovisual data
      does not guarantee quality of service
      functionality:
        payload type identification
        sequence numbering
        timestamping
        delivery monitoring
      augmented by RTCP
        loosely coupled conference control
        data transmission reports

## Slide 11: Technology Multimedia standards
  Session control standards I
    ITU-T H.323
      defines visual telephone system components:
        terminals
        gateways
        gatekeepers
        multipoint controllers
        multipoint processors
        multipoint control units
      specifies control protocols:
        H.245 - control functions
        H.225 - channels definitions

## Slide 12: Technology Multimedia standards
  Session control standards II
    ITU-T T.120
      series of recommendations defining multipoint data conference
        session establishment
        participants identifications and capabilities exchange
        communication channels management
      layered structure
        multipoint communication service (MCS)
        generic conference control (GCC)
        generic application template
        node controller

## Slide 13: Videoconferencing Products Summary
Disadvantages:
  single platform
  point-to-point only
  proprietary compression
  lack of flexibility

## Slide 14: Design and Implementation System Objectives
Flexibility
Interoperability
  platform interoperability
  implementation interoperability
Extensibility
Archiving capability

## Slide 15: Design and Implementation System Architecture
Physical System Components

## Slide 16: Design and Implementation System Architecture
Logical System Structure

## Slide 17: Design and Implementation System Architecture
Multipoint Communication Layer (MCL)
  reliable multipoint channels
  unreliable multipoint channels
Session Control Layer (SCL)
  implemented inside the Conference Engine
  events distribution and handling
  conference information management

## Slide 18: Design and Implementation System Architecture
RTP Layer
  effective processing of media streams
  providing useful information for real-time purposes
Session API
  functions for conference creation and management
  covers the internal manager-engine protocol

## Slide 19: Design and Implementation System Architecture
Application API
  provides useful mechanism for creating new conference application
  developer is concerned only about the data presentation
  important element of system extensibility

## Slide 20: Design and Implementation System Architecture
Session Control Protocol (SCP)
  conference participants management
  conference applications management
  maintaining additional information:
    users directory interconnection
    token mechanism

## Slide 21: Design and Implementation Conference Applications
Audio Tool
Video Tool
Whiteboard
Text Chat
mechanisms for porting arbitrary application

## Slide 22: Design and Implementation Audio Tool
Compression:
  GSM (13 kbps)
  ADPCM (32 kbps)
  PCM (128 kbps)
Architecture
Half-duplex support
Streams buffering and multiplexing

## Slide 23: Design and Implementation Video Tool
Compression:
  H.263 low bandwidth, CPU intensive
  H.261
  H.261 intra - only INTRA frames
  YUV9
Architecture similar to Audio Tool
Frame rate control
Formats conversion

## Slide 24: Design and Implementation Video Tool
Adapting H.261/H.263 codecs
  creating library
  single frame procedures
  converting I/O
  multiple streams handling
  inserting INTRA frame
  performance improvement:
    logarithmic search

## Slide 25: Design and Implementation Directory Service
Active nodes monitoring
On-going sessions advertising
conference creation facilitating
protection and security
session types:
  open
  password protected
  master controlled

## Slide 26: Design and Implementation Archiving
Asynchronous storage mode
System integration:
  application API
  session API
  engine
Database integration

## Slide 27: Design and Implementation Other issues
Java API
  extensibility feature
  multiplatform application
  proof of system flexibility
Session security
  close control model
  data confidentiality
  directory security

## Slide 28: Design and Implementation Web Integration
Tango as collaborative Java environment
BuenaVista vs. Tango
Modifications

## Slide 29: Conclusions System Advantages
Multiuser
Multiplatform
Extensibility
  modular structure
  multilanguage support (APIs)

## Slide 30: Conclusions System Advantages
Flexibility
  several operating modes
  bandwidth control
  Web integration
Archiving capabilities
Interoperability
  standard compliance

## Slide 31: Conclusions Disadvantages and Future Work
Lack of full standard compliance (H.323)
Robustness
Only one session per host
Graphical User Interface (GUI)