## Slide 1: Exploring JSDA, CORBA and HLA based MuTech's for Scalable Televirtual (TVR) Environments
D. Dias[1], G. Fox[2], W. Furmanski[2], V. Mehra[1],
B. Natarajan[2], H.T. Ozdemir[2], S. Pallickara[2], Z. Ozdemir[2]
[1] IBM T.J. Watson Research Center
[2] Northeast Parallel Architectures Center(NPAC) at Syracuse University
Presenter : Hasan Timucin Ozdemir

## Slide 2: TeleVR - Introduction
Java scripting support in VRML2-->VRML97 set the stage for experimenting with multi-user distributed virtual environments on the Internet, hereafter referred to as televirtual, or TeleVR, or shortly TVR environments.
A typical multi-user TVR environments on the internet contain a few VRML browsers(clients), downloading a common VRML world, opening Java node based connections to a collaboratory server which maps user's input such as mouse motions on the suitable movements of the corresponding avatars.

## Slide 3: TeleVR - II
We developed a simple prototype TVR environment of this type at Syracuse University within a joint project with IBM T.J. Watson using JSDA framework for building Java collaboratory services.
Our current TVR prototype has two versions of the VRML+Java front-end: one is based on Script Nodes and the other is based on External Authoring Interface(EAI).
Our current world metaphor is given by a set of rooms with avatars represented by simple geometrical objects (such as colored cones).

## Slide 5: TeleVR - III
We are now adding more realism in terms of more human-like avatars with custom behaviors, conforming to the specifications of the Humanoid Working Group Proposal.
We are also exploring add-on audio-conferencing capability using commodity API's like Microsoft NetMeeting.

## Slide 6: Java Shared Data Architecture - I
Java Shared Data Architecture (JSDA) provides a Shared Framework for Java at the data level.
Data objects are shared over specific instances of Channels (broadcast communication paths) between two or more Clients (objects which are the source or destination of data) in a collaboration environment.

## Slide 7: Java Shared Data Architecture - II
JSDA is a useful framework for prototyping simple collaboratory applications
JSDA does not offer either a wire protocol or a high-level API for client-server communication and messages are typically passed as strings, custom encoded/decoded by JSDA clients/servers.
The family of T12x protocols (which in fact influenced the JSDA design and was adopted by Microsoft's NetMeeting) could be a natural candidate for a TVR protocol.

## Slide 8: CORBA Shared Objects - I
A prototype version of this API using CORBA objects as shared data and CORBA servers as collaboratory servers and Netscape/Visigenic based ORBlet front-ends has been developed.

## Slide 9: CORBA Shared Objects - II
The Client initiates a bind to the PartyScheduler Object.
The Client gets a handle to the Coordinator Object through PartyScheduler interface.
Once the client gets a Coordinator object then it enters a Distributed Collaboration mode, and can invoke operations specified in Coordinator and PartyScheduler interface.
Same API is also developed by using RMI as an underlying technology.

## Slide 10: Scalability and Fault-tolerance
The notion of groups within a certain session allows us to define one object for each group and place these objects on different machines easily.
The ObjectServices agent, which is a distributed directory service, allows for migration of sessions to a different participating host in the case that a session terminates unexpectedly on one of the hosts.
The Events can be stored persistently by the Event Channel to ensure that events are not lost on system failures.

## Slide 11: CORBA Event Service
The Event Service introduces the notion of Event Channel.
Suppliers send events to an Event Channel, and consumers receive these events.
Each channel can have multiple consumers and suppliers, and all events sent by a supplier are made available to all consumers of that channel.

## Slide 12: Collaboration based on Event Service - I
At NPAC, we implemented recently the Event Service for omniORB2, which is a free C++ Object Request Broker under development by Olivetti and Oracle Research Labs.
We wrote the standard Event Service with C++ and omniThread thread library.
We tested this software with a Chat program using the Netscape 3.0 with OrbixWeb based ORBlets.
We also start exploring the issues, related to using CORBA Event Service for Distributed Interactive Simulation (DIS) PDU broadcasting and for HLA/RTI support.

## Slide 13: Collaboration based on Event Service - II
Event Service does not care about the originator of the event but multi-user environments we need this information.
Event Filtering is necessary technique to adjust the frequency of events received from the supplier in large scale interactive simulations.
Event Channel should make this filtering so that the messages are being handled before they are on the network.

## Slide 14: Collaboration based on Event Service - III
Peer-to-peer communication can be done by providing an Event Channel for each active object in the virtual environment so that interested parties can subscribe to these channels.
It is also possible to split the Event Channel if it exceeds the certain capacity and connect two Event Channels to each other.

## Slide 15: Emerging Collaboratory Server Technologies based on DOT
High Level Architecture (HLA) is a next generation framework for distributed simulation systems and promoted by DMSO (Defense Modeling and Simulation Office) to replace the current DIS standard.
HLA's enabling middleware called Runtime Infrastructure (RTI) is based on Distributed Object Technologies(DOT).

## Slide 16: HLA/RTI - I
DMSO is promoting HLA/RTI within the OMG towards a Vertical CORBA Facility for the Interactive Modeling and Simulation.
At NPAC, we are working on:
  An Object Web based implementation of IIOP and HTTP server called JWORB (Java Web Object Request Broker).
  The Object Web based RTI layer to operate on top of JWORB that will provide Web based Simulation support for HLA and a natural linkage to front-end technologies such as VRML.

## Slide 17: HLA/RTI - II
For large geographically distributed M&S systems, middleware must be given by a mesh of scalable collaboratory servers running on heterogeneous platforms and supporting specific simulation components written in various languages.
A Java/CORBA based RTI middleware such as JWORB with VRML front-end seems to offer an attractive pervasive architecture for such systems.

## Slide 18: Conclusion
Communication locality is the necessary element for building scalable multi-user virtual environments on the Internet. This can be achieved with event filtering.
Event filtering is enabled in terms of JSDA channels, CORBA Event service and RTI routing spaces in these technologies.

## Slide 19: Conclusion (Continue)
From these experiences and DMSO’s last attempt, we conclude that CORBA/DCOM based approaches brings the necessary features such as scalability and fault-tolerance.
Object Technology allows us to define each entity in the virtual environment and to integrate with various communication technologies such as JSDA, CORBA/DCOM, or HLA/RTI.
Based on these experiments, we are working on simple/thin layer for multi-user systems so that TVR environments can be defined with less effort and without proprietary protocols.

## Slide 20: URL Addresses
TVR Project Page http://osprey7.npac.syr.edu:1998/iwt98/projects/tvr/intropage/tvr.html
JWORB Project Page
http://osprey7.npac.syr.edu:1998/iwt98/projects/worb/
WebHLA Project page
http://osprey7.npac.syr.edu:1998/iwt98/projects/webhla/